ILA Item# 756565

Cobolt Speechmaster -TalkingTape Measure

FORMAT:  The item is somewhat square in shape with a sloping edge on the left side when the item is held facing you.  A large square button used for retracting the metal tape is found on the sloping edge.   A panel of five small buttons is found on the face of the item.   The first button on the left, top row,is the MR/DISP button.  The second button in the top row on the right is the On/Mode button.   The three buttons in the second row, reading from left to right is the “M+” button, the “MC” button and the “+Case” button.

The belt clip is found at the back of the item.  The battery compartment is found on the straight edge and its indicated by grips just below raised edge where the belt clip is attached on the back of the item.

The features of your tape measure are further described below assuming that you are holding the device with its sloping edge to the upper left and the belt clip facing away from you.

There are five buttons on the front face of the case -

two large ones on the top row and three smaller ones on the bottom row. Pressing any of these will have the effect of turning the unit on.   If the tape is not fully retracted when you turn the unit on you will hear a warning message.

The top left button called “MR/DISP” will advise you of the total distance stored in the memory.   If you press it twice within two seconds the memory will be cleared.

The top right button called “ ON/MODE” is used to switch between feet and inches, millimeters, centimeters and meters. This button will also convert any measurements between these units.

The bottom left button called “ M+” adds the current reading to the memory.  The maximum distance that can be stored in the memory is nine hundred and ninety nine meters.

The bottom center button called “ MC” re-sets the tape to zero.   This can be done with the tape extended to enable you to compare sizes.   It is also possible to measure negative distances in situations where the second measurement is less than the first.

The bottom right button called “+ Case” adds the width of the case to the measurement.   Normally the spoken distance represents the length of the tape which has been pulled out but sometimes It is more convenient to use the back edge of the case- for example if you wish to measure the internal width of a door frame.   A second press of this button deducts the case width and returns the reading to normal.

If the tape is fully retracted the unit will turn off after ten seconds.   In either event you will be warned five seconds before turn off.   Once the tape measure has turned off the current measurement will be lost but the contents of the memory will remain intact.

The tape can be felt protruding from the bottom left edge of the case.  To extend the tape it should be pulled out to the left.  The flat sloping edge is a button used to retract the tape.  This should be pressed at its lower edge.    WARNING Use your free hand to control the speed at which the tape retracts.  If left free it may retract rapidly and cause injury.

On the bottom edge of the case you will feel a deep groove slightly to the right of center, running front to back.   The right side of the base can be pried open using a fingernail in this groove.  This flap can then be opened fully until it is in line with the base.   You will feel a sharp metal point on this flap, which can be used as a pivot if you wish to describe an arc with the tape.   For measurement purposes the point is the same distance from the back of the case as the first hole in the tape is from the end of the tape so if you place the point of a pencil in the first hole and use this to draw a circle or arc the radius will be the measurement spoken which includes the case i.e. to draw a on meter radius circle extend the tape until it says “ one meter including case.”

The battery compartment is on the rear of the case.  To remove the cover, hold the case back uppermost with the sloping edge facing away from you.   Support the case with your fingers underneath and your thumbs on top on the flat section closer to you than the belt clip.   You will feel the ribbed surface of the battery cover under your thumbs.   With your thumbs as close as possible to the edge of the raised section, press firmly down with your thumbs to release the catches and slide the cover off towards you.  Re-fit the cover by sliding it back into place and edge of the door should engage with the back battery compartment on the item and it will click into place.

Specification

Tape length		 	16 feet/5 meters

Max in Memory		999 Meters

Accuracy/ 			1/16th of an inch/1mm

Resolution 			1/16th of an inch/1mm

Battery				1xPP3 9v Alkaline.